## Slide 1: ELE4
CONTROL SYSTEMS
REVISION NOTES

## Slide 2: Systems
Open Loop
  No feedback.
Closed Loop
  Feedback
    Negative
      Reduces the effect of the input
      Output reaches an adjustable steady end point
    Positive
      Increases the effect of the input
      Output oscillates or saturates

## Slide 3: General system
Hunting
Hysteresis

## Slide 4: Microprocessor systems

## Slide 5: Terminology
RAM
ROM
Port
Processor
Clock
Bus
Data Bus
Address Bus
Control Bus
Memory Mapping
I/O Mapping
Read
Write
Volatile
Interrupt
Bit
Byte
Word

## Slide 6: System on a Chip (SoC)
PIC/AVR
RISC
Harvard Architecture
  Separate Instruction Bus
Advantages
  Cheap
  Adaptable

## Slide 7: Flow Charts
Used to determine the sequence of operations required
Aids logical thought

## Slide 8: Q Basic
PRINT
INP
OUT
REM
END
DIM
DO – LOOP – WHILE/UNTIL
FOR – NEXT - STEP
IF – THEN – ELSE
GOSUB – RETURN
INKEY$
INPUT
CLS
GOTO

## Slide 9: Variables
Integer - %
Real
String - $
Arrays

## Slide 10: Neural Networks
Comparison with PC
  NN processors very simple but very many used, traditional computer processors very complex but only a few used.
  NNs retain data in the weightings of the connections made, computers have dedicated memory components.
  NNs are trained - changing the weightings of the connections made with experience, computers follow a pre-described set of instructions.
  NNs best at predictive tasks, computers better at calculations.

## Slide 11: Tristate buffer
  Three states – 0, 1, open circuit
  Enables data to be put onto a data bus without causing ‘bus contentions’
  Output Enable (OE) often ‘active low’
  One needed per bit

## Slide 12: Data Latch
  Enables data to be outputted from data bus
  Processor sets valid data onto data bus and then pulses CK high
  Data captured and stored in latches
  One flip-flop needed per bit.

## Slide 13: Digital to Analogue Converter (DAC)
Usually connected to data bus via a latch
R7 = Rf, R6 = 2Rf,
R5 = 4Rf, R4 = 8Rf,
R3 = 16Rf, R2 = 32Rf,
R1 = 64Rf, R0 = 128Rf

## Slide 14: Analogue to Digital Converter (ADC)
Digital Ramp ADC
Computer increments output from DAC until the analogue voltage is greater than the analogue input voltage
Comparator detects this and ACK is pulled low
Computer detects this and so the last number it sent to the DAC is equivalent to the analogue input voltage

## Slide 15: Flash ADC
Very fast.
Many comparators
    2n-1
Expensive
Uses:-
    Video
    Digital oscilloscopes

## Slide 16: Centronics type port
Base address usually &H378

## Slide 17: Schmitt Trigger
Two switching points
  Hysteresis
  Reduces false switching on noisy signals
Consider as a comparator with a variable reference voltage.
Calculate the voltage at P when the output is high.
  This gives the upper switching point
Calculate the voltage at P when the output is low.
  This gives the lower switching point

## Slide 18: Optical shaft encoders
Resolution:-
  360/2n degrees
  n=number of rings
360/S degrees
  S=number of slots
Optical Shaft Encoder
  Angular direction, speed and absolute position
Slotted Disk (with one sensor)
  Angular speed and relative position

## Slide 19: Photodiodes
Remember LED calculations often included in these questions!
Photodiodes:-
  Can produce a small voltage – 0.6V
  Often used in reverse bias mode
  Reverse bias current proportional to incident light
  Very fast response time (LDRs are very slow)

## Slide 20: Stepper Motor
Rotates through a precise angle
  7.5° for 4 pole motor
  1.8° for 6 pole motor
Needs control electronics to continuously rotate
  Current applied in turn to each set of coils
Less torque and speed of rotation than traditional motor

## Slide 21: Seven segment display
Seven LEDs for segments plus one for the decimal point
Combinations lit to display numbers and characters
  Eg a, b, g, c, d for 3
Standard calculations apply to each LED (segment)

## Slide 22: Dot matrix display
Multiplexed display
  Only one column powered at any one time
  Relies on persistence of vision
  Can be dimmer than normal display since each column is only illuminated for 1/5th of the time
LEDs to be lit are selected via the Row connections as each Column is powered.