## Slide 1: ELEC4
CONTROL SYSTEMS
REVISION NOTES

## Slide 2: Systems
Open Loop
  No feedback.
Closed Loop
  Feedback
    Negative
      Reduces the effect of the input
      Output reaches an adjustable steady end point
    Positive
      Increases the effect of the input
      Output oscillates or saturates

## Slide 3: General system
Hunting
Hysteresis

## Slide 4: Microprocessor systems

## Slide 5: Terminology
RAM
ROM
Port
Processor
Clock
Bus
Data Bus
Address Bus
Control Bus
Memory Mapping
I/O Mapping
Read
Write
Volatile
Interrupt
Bit
Byte
Word

## Slide 6: Tristate buffer
  Three states – 0, 1, open circuit
  Enables data to be put onto a data bus without causing ‘bus contentions’
  Output Enable (OE) often ‘active low’
  One needed per bit

## Slide 7: Data Latch
  Enables data to be outputted from data bus
  Processor sets valid data onto data bus and then pulses CK high
  Data captured and stored in latches
  One flip-flop needed per bit.

## Slide 8: System on a Chip (SoC)
PIC/AVR
RISC
Harvard Architecture
  Separate Instruction Bus
Advantages
  Cheap
  Adaptable

## Slide 9: Flow Charts
Used to determine the sequence of operations required
Aids logical thought

## Slide 10: Assembler Mnemonics
NOP | CALL
RET | INC
DEC | ADDW
ANDW | SUBW
ORW | XORW
JMP | JPZ
JPC | MOVWR
MOVW | MOVRW

## Slide 11: Microcontroller
Clock 1 – 20MHz
8-bit bi-directional ports - PORTA, PORTB and PORTC;
data direction registers TRISA, TRISB and TRISC.
If a bit is set to 1 then the port bit is an input, if the bit is set to 0 then the port bit is an output.
a status register, SR, for which bit 0 is the carry flag, C, bit 2 is the zero flag, Z, and bit 1 is the timer flag;
a clock prescaler, PRE, which can be set to divide the clock frequency by 2 to 256.
an 8-bit timer register, TMR, which is decremented on each falling edge of the clock prescaler pulse and which sets bit 1 of the status register, SR, when it is 0.

## Slide 12: Digital to Analogue Converter (DAC)
Usually connected to data bus via a latch
R7 = Rf, R6 = 2Rf,
R5 = 4Rf, R4 = 8Rf,
R3 = 16Rf, R2 = 32Rf,
R1 = 64Rf, R0 = 128Rf

## Slide 13: Analogue to Digital Converter (ADC)
Digital Ramp ADC
Computer increments output from DAC until the analogue voltage is greater than the analogue input voltage
Comparator detects this and ACK is pulled low
Computer detects this and so the last number it sent to the DAC is equivalent to the analogue input voltage

## Slide 14: Flash ADC
Very fast.
Many comparators
    2n-1
Expensive
Uses:-
    Video
    Digital oscilloscopes

## Slide 15: Photodiodes
Remember LED calculations often included in these questions!
Photodiodes:-
  Can produce a small voltage – 0.6V
  Often used in reverse bias mode
  Reverse bias current proportional to incident light
  Very fast response time (LDRs are very slow)

## Slide 16: Optical shaft encoders
Resolution:-
  360/2n degrees
  n=number of rings
360/S degrees
  S=number of slots
Optical Shaft Encoder
  Angular direction, speed and absolute position
Slotted Disk (with one sensor)
  Angular speed and relative position

## Slide 17: Seven segment display
Seven LEDs for segments plus one for the decimal point
Combinations lit to display numbers and characters
  Eg a, b, g, c, d for 3
Standard calculations apply to each LED (segment)
Multiplexed displays
LCD displays

## Slide 18: Dot matrix display
Multiplexed display
  Only one column powered at any one time
  Relies on persistence of vision
  Can be dimmer than normal display since each column is only illuminated for 1/5th of the time
LEDs to be lit are selected via the Row connections as each Column is powered.

## Slide 19: Stepper Motor
Unipolar and bipolar
Rotates through a precise angle
Needs control electronics to continuously rotate
  Current applied in turn to each set of coils
  H-bridge.
Less torque and angular speed than traditional motor

## Slide 20: Schmitt Trigger
Two switching points
  Hysteresis
  Reduces false switching on noisy signals
Consider as a comparator with a variable reference voltage.
Calculate the voltage at P when the output is high.
  This gives the upper switching point
Calculate the voltage at P when the output is low.
  This gives the lower switching point

## Slide 21: H-Bridge driver
Allows bidirectional control of current
Note the use of p and n channel MOSFETs

## Slide 22: Robotic Systems
Applications
Sensors
Actuators
Control architecture
Power sources
Control algorithms
AI and Neural Networks
Social and economic impact
Future developments

## Slide 23: Neural Networks
Comparison with PC
  NN processors very simple but very many used, traditional computer processors very complex but only a few used.
  NNs retain data in the weightings of the connections made, computers have dedicated memory components.
  NNs are trained - changing the weightings of the connections made with experience, computers follow a pre-described set of instructions.
  NNs best at predictive tasks, computers better at calculations.

## Slide 24: NOTES