## Slide 1: ELEC5
COMMUNICATIONS SYSTEMS
REVISION NOTES

## Slide 2: Generalised System

## Slide 3: Transmission Media Coaxial Cable
  Outer conductor shields inner conductor
  Characteristic Impedance - 50 / 75
  Attenuation – 5dB/10km at 1GHz
      Cable resistance
      Leakage current between conductors
      Radiation of signal
  Velocity ratio = 0.66

## Slide 4: Transmission Media Twisted Pair Cable
  Differential signal
  Characteristic Impedance  100
  Attenuation – 2.2dB/10m at 100MHz
      Cable resistance
      Leakage current between conductors
      Radiation of signal
  Velocity ratio = 0.6

## Slide 5: Transmission Media Free Space
  Electromagnetic waves c=3x108m/s
  Attenuation – 92.4dB/km at 1GHz
  c=f

## Slide 6: Transmission Media Optical Fibre
  Total Internal Reflection
  Attenuation – 3dB/km at 1GHz

## Slide 7: Multiplexing
Enables more information to pass along a communications medium
Frequency Division Multiplexing
    Analogue and Digital Information
    Separate carrier frequency for each signal
Time Division Multiplexing
    Digital Information only
    Separate time slot for each signal

## Slide 8: Signal Degradation
Attenuation
      Ohmic losses
      Radiation
Crosstalk
      Interference from adjacent cables
Dispersion
      Different frequencies travel at different speeds
Distortion
      Signals produced and added to a signal as a signal passes through a communications system
Noise
      Random additional signals added to a signal as it passes through a communications system

## Slide 9: Signal to Noise Ratio
The Decibel – logarithmic ratio
  Add together for each subsystem
Amplification increases both the signal and the noise

## Slide 10: Capacitor reactance
Reactance – the opposition to the flow of alternating current.
Measured in ohms.
Capacitor reactance decreases with frequency.

## Slide 11: Low pass filter
Allows low frequency signals to pass, attenuates high frequency signals
Break point Xc = R

## Slide 12: High pass filter
Allows high frequency signals to pass, attenuates low frequency signals
Break point Xc = R

## Slide 13: Active filter circuits

## Slide 14: Audio power amplifier ICs
The bandwidth of an amplifier is defined as the range of frequencies within which the Power Gain does not fall below HALF of its maximum value.
Power = V2/R, the bandwidth of an amplifier also the range of frequencies within which the Voltage Gain does not fall below 70%, (1/√2) of its maximum value.

## Slide 15: Basic radio system

## Slide 16: Amplitude Modulation (AM)
Frequency constant
Amplitude varies
Broadcast bandwidth is 9kHz
Long and medium wave bands

## Slide 17: Frequency Modulation (FM)
Constant amplitude
Varying frequency
Broadcast bandwidth is 100kHz
VHF wave band

## Slide 18: Signal Bandwidth

## Slide 19: DAB radio
Digital Audio Broadcasting
  More efficient use of radio spectrum
  Tuning by station name
  Transmission of data
  217.5 – 230MHz
  Multiplexes – 2.3Mbits
  National multiplexes
  5+ stations/multiplex – 32kb/s to 192kb/s
  Interleaved audio data over 360ms

## Slide 20: The Simple Receiver
Aerial/earth – changes em waves into electrical signal
Tuned circuit – filters out required signals
Demodulator – removes bottom half of the AM signal
Rf filter – removes the remaining rf signal
Output – recovered information signal

## Slide 21: Tuned Circuits
Quality factor – Q
Resonance when
  XL = XC

## Slide 22: The Simple Receiver -Limitations
Poor selectivity:
  Only one tuned circuit
  Increase the number of tuned circuits
  Difficult to tune several tuned circuits together
Poor sensitivity:
  No amplification – uses energy received by the aerial
  Add rf amplifier
  Add af amplifier

## Slide 23: The Superhet Receiver - 1
The incoming signals are mixed with the local oscillator signal and one of the resulting frequencies is the Intermediate frequency which is filtered and amplified by the if amplifier

## Slide 24: The Superhet Receiver - 2
rf amplifier
    Initial amplification and selection of signals from the aerial
Local oscillator
    Produces difference frequency
Mixer
    Combines local oscillator and radio signal to produce the intermediate frequency (if)
if amplifier
    Contains many tuned circuits and amplifiers
    Provides most of the selectivity and sensitivity for the receiver
Demodulator
    Extracts the information from the carrier
AF amplifier
    Amplifies the information
Automatic Gain Control (AGC)
    Maintains a constant information output as the rf signal varies

## Slide 25: The Superhet Receiver - 3
if frequencies:
    AM receivers – 455kHz
    VHF receivers – 10.7MHz
    Analogue TVs – 39.5MHz
fs + fo = if
    fs = signal frequency
    fo = local oscillator frequency
    if = Intermediate frequency
Image response

## Slide 26: Pulse Amplitude Modulation
Analogue voltage measured at regular time interval and the values transmitted
Sample rate
PAM

## Slide 27: Pulse Width Modulation
Constant amplitude pulses
Width of pulse indicates the magnitude of the analogue signal
PWM

## Slide 28: Pulse Position Modulation
The pulses are of constant amplitude and duration
The pulses are delayed at each sample by an amount that is dependent upon the amplitude of the signal
PPM

## Slide 29: Pulse Code Modulation
The amplitude of the analogue signal is sampled
The sample is then converted into a binary value by an ADC
The binary value is transmitted in serial form
PCM

## Slide 30: Packet Switching
  More efficient use of network
  Data broken into blocks – packets
  Ethernet – GPRS – Land line telephone
  Header – Data – Checksum
  Packet switching network – Routers
  Transmission by different paths
  Receiver assembles packets in order
  Redundancy within packet switching network

## Slide 31: Serial Transmission - 1
Serial v Parallel
Half Duplex
    One device transmits, the other receives
    Only one transmission medium is needed
Full Duplex
    Both devices transmit and receive at the same time
    Two transmission media are needed
Synchronous / Asynchronous
Handshaking
    RTS CTS

## Slide 32: Serial Transmission - 2
6510 (001000012)
Start bit
Stop bit(s)
Parity bit
Baud rate
Bit rate

## Slide 33: Serial Transmission - 3 The Shift Register
On the rising edge of each clock pulse, the data from a D-type flip-flop is stored in the next D-type flip-flop.
This data transfer occurs all of the way along the shift register.
Data from the output of the last flip-flop is lost.
New data applied to the input of the first flip-flop is taken into the shift register.
Timing diagrams

## Slide 34: Multiplexers
Multiplexer Demultiplexer
Both need a clock and a two bit counter

## Slide 35: Cellular Communication
Very short communication by radio from mobile handset to base station
Repeater
Regenerator
Frequency reuse
Cell size depends on the number of channels required
Separate up link and down link frequencies
GSM – 900MHz, DECT – 1.8GHz, 3G – 2GHz

## Slide 36: Fibre Optic Communication
Laser diode transmitters 0.9 – 1.6m
PIN diode receivers
Dispersion
Total Internal Reflection
Attenuation
    Scattering
    Absorption
    Radiation
Compare with wired systems