## Slide 1: ELE2
ANALOGUE
REVISION NOTES

## Slide 2: OP-AMPs
Differential amplifier
Large input resistance 109
Large open-loop voltage gain, A,  106
Low output resistance  100
Frequency compensated
Gain-bandwidth product

## Slide 3: Inverting Amplifier
Input resistance = R1
Output inverted
Virtual earth point
Saturation/clipping
Bandwidth/voltage gain
Minimum resistance 1k

## Slide 4: Summing Amplifier
Recognise by multiple inputs
Input resistance of each input = R
Behaves the same as the inverting amplifier
Used in DAC & Mixer

## Slide 5: Non-inverting amplifier
Very large input resistance  109
Beware input resistor to 0V
Output in phase with input
Voltage gain/bandwidth
Minimum voltage gain = 1
Voltage follower when Rf = 0 or R1=

## Slide 6: Source Follower
Voltage gain  0.7 – 1
Current gain  109
Output voltage in phase with input
Very large input resistance  109
Remember to subtract Vgs from Vin to obtain Vout
N-channel and p-channel

## Slide 7: Push-pull amplifier 1
Provides power gain
Needs op-amp to provide voltage gain
Cross-over distortion at low volume
Bias MOSFETs into conduction
Saturation/clipping at high volume
Increase supply voltage or reduce input voltage

## Slide 8: Push-pull amplifier 2
Negative feedback
Heat sinks
  Metal
    conduction
  Black
    radiation
  Large surface area
    Convection
    Radiation
  Fan
    Convection

## Slide 9: Capacitor reactance
Reactance – the opposition to the flow of alternating current.
Measured in ohms.
Capacitor reactance decreases with frequency.

## Slide 10: Low pass filter
Allows low frequency signals to pass, attenuates high frequency signals
Break point Xc = R

## Slide 11: High pass filter
Allows high frequency signals to pass, attenuates low frequency signals
Break point Xc = R

## Slide 12: ELE2 Questions
Set in context – read the context – underline relevant details.
Look carefully at circuit diagrams – circle and name sub-systems.
Focus on relevant bookwork descriptions and calculations – answer these.
Attempt all sections – no credit can be given if there is no attempt at an answer.
Estimate, Calculate – show your working.
State and explain – do both!