## Slide 1: ELE2
DIGITAL
REVISION NOTES

## Slide 2: Bistable Latch
When the SET input is briefly taken to logic 0, the Q output will become logic 1 and the output will become logic 0.
When the RESET input is now briefly taken to logic 0, Q will become logic 0 and the will become logic 1.

## Slide 3: NAND Gate Monostable
When input of gate X goes low the output of gate X goes high.
This starts to charge capacitor C through resistor R and so makes the input of gate Y high.
The output of gate Y goes low, which is fed back to gate X so keeping its output high.
C charges through R until the input voltage to gate Y is below half of the supply voltage.
The output of gate Y goes high, making output of gate X low, circuit resets.
TRC

## Slide 4: NAND Gate Astable
Control input to first NAND gate goes high.
Output of first NAND gate goes low, output of astable goes high.
Capacitor discharges and charges in opposite direction.
Until voltage at input to first NAND gate <+Vs/2.
Output of astable switches state.
Capacitor charges in opposite direction.
Process repeats as long as control is high.
T2RC
f=1/T

## Slide 5: D-Type Flip-Flop
S sets Q to 1, R resets Q to 0. Not dependent on the state of the clock, CK.
On the rising edge of CK, Q is set to the logic state of D.

## Slide 6: Data Latch
The data to be stored in the latch is set up on inputs D0 to D3.
When the data is steady, a short pulse is applied to the clock inputs.
The data is stored in the latch on the rising edge of the clock pulse.

## Slide 7: Shift Register
On the rising edge of each clock pulse, the data from a D-type flip-flop is stored in the next D-type flip-flop.
This data transfer occurs all of the way along the shift register.
Data from the output of the last flip-flop is lost.
New data applied to the input of the first flip-flop is taken into the shift register.

## Slide 8: Divide by 2 Counter
The D input is then always opposite to Q and so toggling occurs on each successive clock pulse.
To make a flip-flop toggle:-
Both Set and Reset are connected to 0
D is connected to

## Slide 9: 4-bit Counters
D to
All Resets joined together
CK to previous Q for down counter and for an up counter
All resets joined together and connected to 0

## Slide 10: Modulo-n Counters
Only up-counters.
AND gate output connected to reset.
AND gate inputs connected to appropriate Q outputs.
5, Q0 & Q2 6, Q1 & Q2 10, Q1 & Q3 12, Q2 & Q3

## Slide 11: Boolean Algebra
Commutative Laws:
    A + B = B + A A · B = B · A
Associative Laws:
    A + (B + C) = (A + B) + C A ·(B · C) = (A · B) · C
Distributive Law:
    A · (B + C) = A · B + A · C
De Morgan's theorem

## Slide 12: Boolean Identities
Karnaugh Maps